PCB111000_CP2102_projects \AVR_freaks_second_posting\Projects	Test results

1_first_project

All examples successfully recompiled

Example 1	OK
Example 2	OK
Example 3	OK
Example 4	OK
Example 5	OK
Example 6	OK
Example 7	OK
Example 8	OK
Example 9	OK
Example 10	OK
Example 11	OK

Also checked:	Commentary input and readout
User project reset
Intensity control
Recal_328_using_crystal.ino.standard
cal_one_wire_comms.ino.standard

PRN_16bit_GEN() and bootloader\1_Random_pattern_generator
both write to one of 3 pairs of EEPROM registers
Press E at p/r/t/D prompt to change EEPROM register pair

2_Receiver_Transmitter_Basic

All examples successfully recompiled

Example 1	OK
Example 2	OK
Example 3	OK
Example 4	OK
Example 5	OK
Example 6	OK
Example 7	OK
Example 8	OK
Example 9	OK

3_Interrupts_and_switches

3A_UART_timer_interrupts	Recompiled	OK
3B_Pin_Change_Interrupt	Recompiled	OK
3C_reaction_time_tester	Recompiled	OK
3D_timer_PCI_interrupts	Recompiled	OK
3E_Keypress_logger	Recompiled	OK
3F_Prime_numbers	Recompiled	OK
3G_Prime_numbers_plus	New project	OK
4_binary_and_bit_operations

1_Bit_ops_1	Recompiled	OK
2_Bit_ops_2	Recompiled	OK
3_Division_subroutine	Recompiled	OK
4_Char_to_binary	Recompiled	OK but to be reviewed

5_Arduino_PC_comms_library	Arduino_Rx_Tx.c update: DONE
All recompiled: To be retested
5A_Integer_numbers	All factors	Recompiled	Tested OK
5B_Prime_factors	Prime factors	Recompiled	Tested OK
5C_Scientific_numbers	Raise to power	Rewritten	Tested OK
5D_Pie_estimator	Pie_estimator	Recompiled	Tested OK
5E_e_power_series	Calculate power(A,B)	Recompiled	Tested OK
5F_Trig_functions	New project	Recompiled	Tested OK

Bugs found in Arduino_Rx_Tx.c
Bug 1
Int_Num_from_PC_A() for /b keypress.
Sc_Num_from_PC_A() with \b keypresses

For example 12345\b6 comes to a halt and times out
Also 1mS delay increased to 10mS

Bug_2 found in Sc_Num_to_PC_A()
Fails for Sc_Num_to_PC_A(Result,0,6,'\r');	The 0 must be at least 1

Bugs partially fixed
9_Resource_store\PC_comms\Arduino_Rx_Tx.c	NOT yet fully updated

Remember:
Always update Arduino_Rx_Tx.c in future projects when used
Also update equivalent files in PCB111000_UNO_V2 for both UNO and Arduino projects

6_The_8_digit_display_and_IO To be retested

6A_Segment_driver	Recompiled
6B_Segment_driver	Recompiled
6C_Numerical_entry	Recompiled
6D_INT_to_display	Updated to Running averages	Recompiled
6E_FPN_to_display	Updated to power series	Recompiled
6F_FPN_from_IO	Updated to power series	Recompiled
6G_INT_from_IO	Updated geometric series	Recompiled
6H_calculator	New project	Recompiled

In Arduino_Rx_Tx.c
void Sc_Num_to_PC_A(float, char, char, char) updated as below

if(pre_dp){
while(--pre_dp){A = A*10;}	//Convert FPN to Scientific format (real + exponent)
while (num >= A){num = num/10.0; Exp += 1;}
while (num <= A){num = num*10.0; Exp -= 1;}}
In 6F_FPN_from_IO and 6H_Calculator
float FPN_number_from_IO(void) updated as below

dp_control = 0;
exp_control = 0;
neg_sign = 0;
scroll_control = 0;

7_Timers	update Arduino_Rx_Tx.c

8_Resets	update Arduino_Rx_Tx.c

9_FPN_routines	update Arduino_Rx_Tx.c